## Slide 1
FARMWORKER HOUSING
PROTECTING PUBLIC ENVIRONMENTAL HEALTH-PROPOSALS
Heather Forshey, Director
Ed Diaz, Supervisor, Land Use Programs
Maria Gomez-Casillas, Lead, Water Programs

## Slide 2
Findings from the Farm Labor Housing Task Force, 2023-2024 :
During the safety checks conducted on 145 farm labor housing units, lack of safe drinking water and concerns with wastewater disposal were two of the most cited issues
21 Water systems serving an estimated 35 farm labor housing units tested positive for the presence of total coliforms and/or E. coli

## Slide 3
Findings from the Farm Labor Housing Task Force :
Eight boil water notices were issued for the presence of Total coliforms or E. coli until repairs were performed and resampling confirmed water was potable
Waste water disposal serving eighteen occupied farm labor housing units required corrective action (i.e., repair or construct OWTS)
Notes: Action items included repairing/replacing treatment units such as UV treatment units, replacing plumbing, and replacing well caps so they were adequately secured to the top of the well to prevent contamination.
Samples are taken to state certified laboratory. If TC is present, repeat samples (within 24 hours) until negative. If E.coli is present, treatment is required (and issuance of boil water notice) to inactivate the pathogen. Once tested negative, boil water notice can be lifted (Notification of lifted Boil Water Notice will be issued by the Division).
Presence of total coliform can indicate that there is a source of contamination in the water system, either directly from the source (i.e. the supply well/spring or distribution components (i.e. piping, storage etc.) and/or a lack of proper disinfection of the water.

## Slide 4
IMPROVE DRINKING WATER for RESIDENTS:
BACKGROUND:
Public water systems (regulated by State) 15+ service connections (or 25+ regular users)
State Small water systems (regulated by EHS) 5-14 service connections
Domestic wells/water sources that serve 1-4 connections are not regulated once initial water quality (post construction) demonstrates that the water from the well/water source meets drinking water standards
Notes: •Community Water System: a public water system that serves at least 15 service connections used by yearlong residents or regularly serves at least 25 yearlong residents of the area served by the system
•Non-Transient Non-community Water System: a public water system that is not a community water system and that regulates at least 25 of the same persons over six months per year.
•Transient Non-community Water System: a non-community water system that does not regularly serve at least 25 of the same persons over six months per year.
State Small Water System: a system for the provision of piped water to the public for human consumption that serves at least five(5), but no more that fourteen (14), service connections and does not regularly serve drinking water to more than an average of 25 individuals daily for more than 60 days out of the year

## Slide 5
IMPROVE DRINKING WATER for RESIDENTS:
Resources:
The Farm Labor Housing Task Force Report can be found at www.smcgov.org/planning/farm-labor-housing-compliance
Additional information regarding Public Water Systems: https://www.waterboards.ca.gov/drinking_water/programs/
Public Water Systems regulations can be found on the State Water Resource Control Board’s website at: https://www.waterboards.ca.gov/drinking_water/certlic/drinkingwater/Lawbook.html
Notes: •State Small Water System: a system for the provision of piped water to the public for human consumption that serves at least five(5), but no more that fourteen (14), service connections and does not regularly serve drinking water to more than an average of 25 individuals daily for more than 60 days out of the year

## Slide 6
IMPROVE DRINKING WATER for RESIDENTS:
NEW: Farm Labor Housing water system (proposed) 1-4 service connections that serve at least 1 Farm Labor housing unit
A Farm Labor Housing Water System: defined as a system serving at least one (1), but not more than four (4) service connections, of which at least one connection serves a farm labor housing unit.

## Slide 7
IMPROVE DRINKING WATER for RESIDENTS:
Farm Labor Housing as defined by the San Mateo County Planning and Building Dept’s “Farm Labor Housing Policy”: housing units that can only be occupied by farm laborers and their immediate family members. This includes properties that choose not to enroll in the San Mateo County Planning Department Farm Labor Housing Permitting Program but are eligible for the program based on Planning Department zoning districts.
Notes: Per Planning and Building Department the mentioned zoning districts are land use zoning districts which preserve and foster existing and potential agricultural operations (Zoning Regulations PAD Section 6350); and fulfill the requirements for Open Space and Conservation Elements of the County’s General Plan (Zoning Regulations RM Section 6310; RM-CZ Section 6900).
If in the coastal zone; a coastal development permit will be required.
Eligible zoning districts referenced in the Planning and Building Farm Labor Housing Guidebook (which pulls source from Farm Labor Housing Policy) as:
  Planned Agricultural District/Coastal Development (PAD/CD);
  Resource Management District-Coastal Zone/Coastal Development (RM-CZ/CD);
  Resource Management District (RM)

## Slide 8
IMPROVE DRINKING WATER for RESIDENTS:
Zoning Districts subject to County’s Farm Labor Housing Permitting Program (from County Farm Labor Housing Policy):
  Planned Agricultural District (PAD);
  Resource Management District (RM);
  Timberland Preserve Zone (TPZ)
Notes: Flexible treatment options such as POU and POE
Per San Mateo County Planning and Building Farm Labor Housing Guidebook, a land use permit is required for development in the County's Coastal Zone in conformance with the County's Local Coastal Program (LCP). Development in the Coastal Zone requires either a CDP or a Coastal Development Exemption (CDX).
Eligible zoning districts referenced in the Planning and Building Farm Labor Housing Guidebook (which pulls source from Farm Labor Housing Policy) as: Planned Agricultural District/Coastal Development (PAD/CD); • Resource Management District-Coastal Zone/Coastal Development (RM-CZ/CD); • Resource Management District (RM)
Summer provided more insight on what districts are allowed for FLH permits. Essentially there are 3 zoning districts that qualify for FLH permits. They are PAD, RM, and TPZ(Timberland Preserve Zone) districts. PAD is only in the coastal zone, RM & TPZ are both inside and outside the coastal zone (inside “C”oastal “Z”one: RM-CZ, TPZ-CZ, outside: RM, TPZ).

## Slide 9
IMPROVE DRINKING WATER for RESIDENTS:
Extend the protection provided to residents with State Small systems to residents with Farm Labor Housing water systems
Require ongoing water sampling to be collected by the owner and/or designee of the water system for bacteria (annually or more often if issues exist) and for other contaminants, if they are identified (e.g., Nitrates)
Subject to regular inspections aligned with State Small Systems (triennially, more often if there is treatment installed, surface water is used, or there are issues)
Notes: Total Coliform and E.coli (bacteriological sampling) will be required quarterly for State Small Water Systems unless otherwise noted.
For Farm Labor Housing Water Systems Total Coliform and E.Coli will be required to be sampled at least once a year unless otherwise noted. Positive bacteriological results will trigger additional testing.
Nitrate/Nitrite will be sampled once during initial sampling unless otherwise deemed by the Division. Similar to Total coliform and E.coli, if present for Nitrate/Nitrite repeat sampling will be required. If Nitrate sample exceeds MCL, operator must notify this DIvison within 24 hours of know result. More frequent monitoring and reporting may be required by the Division to ensure drinking water standards are met.
Regulations for State Small Water Systems California Code of Regulations (CCR) Title 22 Section 64212, California Health and Safety Code

## Slide 10
IMPROVE DRINKING WATER:
50+- eligible for oversight of Farm-Labor Housing Water System (1-4 service connections)—2 years to get program off ground
Annual permit with associated fee will be required to cover cost of program: Annual Permit COST approx: $2300
No permit fees thru June 2027; looking for ways to extend fee relief further
Notes: 7 hours/year @$328/hr $2296 (January 2026)
For program that includes 1 bacti/yr, monitoring, reminders, complaints, inventory management w/ no routine inspection =1.6hr/yr @328/hr=$525
FTE covered by NCC thru 6/2027 being used to support FLH taskforce can incorporate the start up w/ no revenue from fees

## Slide 11
INCREASE OPTIONS FOR OWTS DESIGNS:
Minor changes to OWTS installation/design manual (this does not require BOS vote):
  Allow for minimum 1 and 2 bedroom design instead of the required 3 bedroom design under residential requirements allowing more flexibility for development.
  “Farm labor housing unit” is added under residential system sizing and secondary dwelling units of less than 750sqft. (i.e., FLH is treated the same as ADUs when connecting to existing systems.)
In coordination with RWQCB: OWTS Ordinance will be reviewed for potential updates

## Slide 12
Minor updates to OWTS OSM: (weeks)
Water System Ordinance changes: BOS Dec 2025
Implementation of FLH Water System Program: upon approval from BOS
TIMELINE:

## Slide 13
Questions?