## Slide 1
Energy and Water Savings
Presented by Bill Power
Power Services, Inc.
2014 San Mateo County Ag Workshop
December 5, 2014

## Slide 2: Pump Efficiency
If you repair your pump PG&E will help with the cost through their Advanced Pump Efficiency Program.
Example:
1000 Hrs. 80 PSI $.18 cost per kWh
Average OPE of pumps in area is 46% should be 63%
If repair is made you could save 8200 kWh or $1475.00
per year

## Slide 3: Irrigation System Improvement
If you repair your system NRCS may be able to help with the cost through their EQIP Program
Example:
25 acres Crop use 15 inches $.18 cost per kWh
Average DU of systems in area is 45% should be 80%
If repair is made you could save 6100 kWh or $1100.00
per year

## Slide 4: Undersized Mainline
If you replace your 4 inch mainline NRCS may be able to help with the cost through their EQIP Program
Example:
4 inch pipe, 400 GPM, 1000 hours,20 PSI pressure drop $.18 cost per kWh
Switching to 6 inch mainline could save 17,650 kWh or $3200.00 per year

## Slide 5: Variable Frequency Drive
PG&E has rebate program to help with cost.
When speed is reduced to 75 percent of design speed, flow decreases to 75 percent, outlet pressure decreases to 56 percent, and the input power requirement drops to 42 percent of full-speed values.
Even small reductions in speed and flow can result in significant energy savings.

## Slide 6: Energy Efficient Motors
PG&E has rebate program to help with cost.
1000 hours per year and $.18 cost per kWh
25 HP Saves about $111.00
50 HP saves about $172.00